## Slide 1: Road Tunnels Air Quality Considerations Community Meeting - Balgowlah Golf Club
Noel Child (NG Child & Associates)
Thursday November 22nd 2018

## Slide 2: Existing Sydney Road Tunnels

## Slide 3: New Developments

## Slide 4: Existing Sydney Road Tunnels
TUNNEL | LENGTH | VENTILATION | STACKS | AIR TREATMENT
Harbour | 2.3 km | Transverse | 1 | None
Eastern Distributor | 1.7 km | Longitudinal | 1 | None
M5 East | 4.0 km | Longitudinal | 1 | None (Note 1)
Lane Cove | 3.6 km | Longitudinal | 2 | None (Note 2)
Cross City | 2.1 km | Longitudinal | 1 | None (Note 3)
Note 1: ESP & DeNOX system trialled Note 2: Capacity for air treatment included in design Note 3: Capacity for air treatment included in design |  |  |  | 

## Slide 5: New Tunnels … getting longer & busier
North Connex Details (a typical example)
    Length: 9.2 km
    Lanes: 3 in each direction (two initially)
    Ventilation: Longitudinal
    Air Treatment: None proposed
    Emission Stacks: One at each end

## Slide 6: Some Air Quality Issues
In Tunnel
External
Pollutants of Concern
      Carbon Monoxide
      Nitrogen Dioxide
      Hydrocarbon Residues
      Fine Particulates (PM10 & PM2.5)

## Slide 7: Ventilation & Air Quality Options
          Ventilation
            Longitudinal
            Transverse
          Air Cleaning
            Particulates
            Hydrocarbon Residues
            Nitrogen Dioxide

## Slide 8: Ventilation Options
Longitudinal
Transverse

## Slide 9: Air Treatment Options
Fine Particulates
Electrostatic Precipitation
NOX & Hydrocarbons
Catalytic Processes

## Slide 10: Air Cleaning Efficiencies
Tokyo Tunnel Example

## Slide 11: Air Treatment Volumes
 | TOKYO SHINJUKU LINE | MADRID CALLE 30 | M5 EAST TEST PLANT
Total ESP Volume (M3/Sec) | 3509 | 5404 | 200
TOTAL DeNO2 Volume (M3/SEC) | 3509 | 2114 | 50
Total Treatment Volume (M3/Sec) | 7018 | 5404 | 200

## Slide 12: New Tunnels … getting longer & busier
North Connex Details (a typical example)
    Length: 9.2 km
    Lanes: 3 in each direction (two initially)
    Ventilation: Longitudinal
    Air Treatment: None proposed
    Emission Stacks: One at each end

## Slide 13: International Experience
TECHNOLOGY: Air treatment proven & established for appropriate applications Ventilation method selected on a performance basis
SPAIN: Extensive evaluation of “long tunnel” ventilation and air treatment technologies in Madrid – various ventilation methods and air treatment technologies adopted
JAPAN: Recent Tokyo metropolitan road tunnel a good case study – Yamate Tunnel 18 kilometres in total comprising separate 8 km and 10 km tunnel sections – transverse ventilation and air treatment incorporated
STOCKHOLM: Proposed E4 By-Pass Tunnel – longitudinal ventilation but complete air exchange every three kilometres

## Slide 14: NSW Approach
VENTILATION: All tunnels longitudinally ventilated
AIR TREATMENT: Air treatment technology “not RMS policy”

## Slide 15: Key Considerations
POLICY
  A Balanced & Integrated Approach
  Roads + Rail – NOT Road Only
  Treat the public as a genuine stakeholder
  Good Process Essential
AIR QUALITY
  Air Quality Must be Safeguarded
  Stacks and “Filtration”
  Stack Locations
  Air Quality Monitoring – In-Tunnel and External
VENTILATION
  Appropriate Tunnel Ventilation
  Proposed Ventilation Method a Potential Concern
  Ventilation & Air Quality Linked
  Minimum Cost/Maximum Profit Approach Risky

## Slide 16: The Issues
ALTERNATIVES NOT CONSIDERED
TUNNEL VENTILATION
EXHAUST EMISSIONS
HEALTH IMPACTS
  CONCERNS FROM KEY GOVERNMENT AGENCIES
  CONCERNS FROM THE MEDICAL PROFESSION
  CONCERNS FROM REGULATORS
CONTEMPT FOR THE PUBLIC

## Slide 17: The Solutions
GOOD PROCESS
CONSIDER THE OPTIONS
APPROPRIATE TUNNEL VENTILATION
EXHAUST AIR TREATMENT IF NEEDED
  INDEPENDENT AIR QUALITY MONITORING
  INDEPENDENT OVERSIGHT
  TRANSPORT POLICY PRIORITIES
  RESPECT FOR THE PUBLIC